## Slide 1: Phytoplankton Sampling Protocols Development Department of Environmental Quality Division of Water Resources
July 31st, 2018

## Slide 2: Why do we need them?
Algal blooms occur in the Cape Fear River
  Algae known to produce toxins
  Large long river
Monitoring/Assessing blooms requires multiple agencies
  2013 Seventy one miles of visible flecks and swirls
    Coordinated response:
      DWR (WSS, FRO, WiRO) Coalitions (MCFRBA & LCFRP), ACOE, PWS, WTP & DPH
  2015 Bloom reported after the Toledo water crisis
    Coordinated response:
      DWR (WSS, WiRO), PWS, DPH, WTPs, & Coalitions (MCFRBA & LCFRP)
Cape Fear River Water Quality Model Development

## Slide 3: Current protocols insufficient
Developed for routine monitoring
Episodic protocols too general
  Encompasses all algae, aquatic plants and related organisms
  Random bottles (i.e. Water, Gatorade, gelato)
Health concerns not major focus
Needs to address
  In-house Cyanotoxin analytical capabilities
  Collection and handling important!
  Quality Assurance
  Results must be legally defensible

## Slide 4: Algae Basics
Not plants!
Diverse group of somewhat related organisms
Algae forms: Phytoplankton, Filamentous & Periphyton
Procedures concentrate on phytoplankton:
  Algae in water column
  Concentration varies
    Spatial and temporal
    Quantification/Densities
  Blooms move!
    Flowing water
    Wind and waves

## Slide 5: How difficult can it be?
Find a bloom
Put it in a bottle
Send it to a phycologist
  How many phycologists do you know?
Everything relies on:
  Communication
  Coordination
  Contacts
  PRACTICE!

## Slide 6: Challenges
What do you sample?
  Water column
    Photic vs grab
  Surface film
Shipping and handling
When to preservative
  Quantification requires it
  Toxin analysis? Maybe.
    Recreational: no
    Finished drinking water: yes

## Slide 7: What is the question?
Multiple protocols to select from
  Photic vs grab
    Quantification
  Surface scoop
Exposure risk assessment
  Recreational
    Shoreline, surface & water column
  Aquatic life
    Water column
  Drinking water
    Source (raw) and finished
Division of Public Health: Health Risk Evaluations (HREs)
  HREs based on:
    Cell counts
    Toxin levels (ug/L or ppb)
May (often) require more than one sample

## Slide 8: Supplies, Equipment & Documents
Draft Algal Bloom and Cyanotoxin
  - Field Collection and Response Protocol
Sample collection form
Physical parameters: meters
  Dissolved oxygen & pH
Chemical parameters: bottles and coolers
  Chlorophyll-a & nutrients
Phytoplankton:
  Bottle selection important
    Disposable
      lugol’s solution stains
    PTEG
      Reusable
      Wash
    Glass amber

## Slide 9: Cyanotoxin Testing Development
Field Staff/Regional Office
  Abraxis cyanotoxin test strips
    Rapid assessment
    Field or office use
    Available for a range of toxins
    Freshwater, marine, recreational & finished drinking water
    Currently evaluating Microcystin recreational (10 µg/L)
Water Sciences Section Chemistry Laboratory
  Abraxis Cyanotoxin Automated Assay System
    ELIZA instrument
    Quality assurance and Quality Control procedures
    sample collection, handling & processing procedures

## Slide 10: Conclusion
Phyto sampling protocols needed
  Can be field tested
  Multiple agencies/organizations can follow
  Blooms can be better documented
  Exposure risks be better evaluated
  Data is comparable
  Data is defensible

## Slide 11: Contact Information: Ecosystems Branch
Brian Wrenn: Supervisor
  brian.wrenn@ncdenr.gov
  (919) 743-8409
Leigh Stevenson
  leigh.Stevenson@ncdenr.gov
  (919) 743-8451
Elizabeth Fensin
  elizabeth.Fensin@ncdenr.gov
  (919) 743-8421
Mark Vander Borgh
  mark.vanderborgh@ncdenr.gov
  (919) 743-8423